## Slide 1: RTOS REVIEW
COURSE PROJECT
CAR PARKING BARRICADE SYSTEM
NAME | ROLL NO.
Rahul Sajjan | 121
Vinayak Bhajantri | 125
Vinayak Jainapur | 140
Abdul Razzak R Yergatti | 142
RTOS Team F11

## Slide 2: PROBLEM STATEMENT
In Car Parking lots and Parking Garages, entry is controlled using barrier systems. The barrier must not be lowered when there is a vehicle underneath. Devise a system to implement the same on Cortex M3 board (LPC 1768).

## Slide 3: PERIPHERALS USED AND ITS SPECIFICATIONS
ON-CHIP PERIPHERALS
  RTC
    An ultra-low power 32 kHz oscillator will provide a 1 Hz clock to the time counting portion of the RTC.
    The RTC includes an alarm function that can wake up the LPC17xx from all reduced power modes with a time resolution of 1 s.
    Dedicated power supply pin can be connected to a battery or to the main 3.3 V. RTC power supply is isolated from the rest of the chip.
    Measures the passage of time to maintain a calendar and clock.
    • Dedicated power supply pin can be connected to a battery or to the main 3.3 V.
    • Periodic interrupts can be generated from increments of any field of the time registers.
    • Backup registers (20 bytes) powered by VBAT.

## Slide 4: PERIPHERALS USED AND ITS SPECIFICATIONS
  UART
      The board has an RS-232 serial communication port.
      The RS-232 transmits and receives signals that appear on the female 9-pin DB connectors (DB3).
      It uses a standard RS-232 cross cable to connect the board to the computer's serial port.
      The controller U1 provides serial I/O data at TTL levels to the MAX232 (U13) device, which in turn converts the logic value to the appropriate RS-232 voltage level.

## Slide 5: PERIPHERALS USED AND ITS SPECIFICATIONS
  LCD
    The operating voltage of this display ranges from 4.7V to 5.3V
    The display bezel is 72 x 25mm
    The operating current is 1mA without a backlight
    PCB size of the module is 80L x 36W x 10H mm
    LED color for backlight is green or blue
    Number of columns – 16
    Number of rows – 2
    Characters – 32
    It works in 4-bit and 8-bit modes

## Slide 6: PERIPHERALS USED AND ITS SPECIFICATIONS
OFF-CHIP PERIPHERALS
  ULTRASONIC SENSOR
    Supply voltage: 5V (DC)
    Supply current: 15mA
    Modulation frequency: 40Hz
    Output: 0–5V
    Beam angle: Max 15 degrees
    Distance: 2 cm–400 cm
    Accuracy: 0.3 cm
    Communication: Positive TTL pulse
  STEPPER MOTOR
    Rated voltage: 5V DC
    Reduction Ratio: 64:1
    Step Angle: 5.625° /64
    Self-positioning Torque: >34.3mN.m
    Friction torque: 600-1200 gf.cm.

## Slide 7: FLOWCHART
YES
NO
YES
NO

## Slide 8: BLOCK DIAGRAM

## Slide 9
PROGRAM

## Slide 10
PROGRAM

## Slide 11
PROGRAM

## Slide 12
PROGRAM

## Slide 13
PROGRAM

## Slide 14
PROGRAM

## Slide 15
PROGRAM

## Slide 16
PROGRAM

## Slide 17
PROGRAM

## Slide 18
PROGRAM

## Slide 19
PROGRAM

## Slide 20
PROGRAM

## Slide 21
PROGRAM

## Slide 22
PROGRAM

## Slide 23
PROGRAM

## Slide 24
PROGRAM

## Slide 25: RESULTS VIDEO

## Slide 26: THANK YOU
RTOS Team F11